## Slide 1
PROJECT FOR ELECTRONICS LAB (ECE 211P)
COLOR SENSING AND SORTING CONVEYOR SYSTEM

## Slide 2
  A color sensing sorting conveyor system which sorts objects based on color matching criteria, and also give real time feedback on an 16x2 LCD screen.
  2 Arduino Uno microcontroller boards have been programmed for this project.
  This project has three main parts: The conveyor system, the color sensing and LCD display, and the IR sensors & servo flap system.

## Slide 3
TEAM MEMBERS:
  Karan Kandpal (BT2024194)
  R S Tarun (BT2024198)
  Akshat Kashyap (BT2024269)
  Pranava Swarup Balachander (IMT2024072)
  Saarthak Singh (IMT2024082)
  Anirudh R Rao (IMT2024083)
  Puttaraja Beedinalmath (IMT2024091)

## Slide 4
Components Used:
  TCS3200 color sensor
  12V 60 RPM DC motor
  SG90 servo motors
  cardboard
  wires
  arduino Uno
  Batteries
  5V single channel relay module
  resistances
  breadboard

## Slide 5
OBJECT CONTROLLED CONVEYOR SYSTEM

## Slide 6
  A simple object-controlled cardboard conveyor system.
  A 12V 60 RPM DC motor connected to battery and controlled by a relay module.
  Relay module works as a switch turning the power to the motor ON/OFF, based off the input given via one of the Arduino Uno used.

## Slide 7
COLOR DETECTION AND REAL TIME DISPLAY

## Slide 8
  A TCS3200 color sensor is used to detect the color of the object.
  Depending on the values set manually, the RGB values are read from the sensor and a color is decided : red, blue, green.
  In case the set values are not matched, the object color is decided black/white and is discarded (not sorted)

## Slide 9
IR SENSORS AND SERVO FLAP
SORTING

## Slide 10
  There are 3 IR sensors and 3 SG90 servo motors on the either side of the conveyor belt, each mapped to one of the aforementioned colors.
  Once the color sensor detects a color the respective IR sensor value is read. Rest are ignored.
  In case the no color is assigned, all IR sensors are ignored.

## Slide 11
  Similarly the servo motor mapped to the color is also armed in a “blocking” position.
  Once the mapped IR sensor detects the object, the relay module stops the conveyor system for 500 milliseconds.
  The servo motor then pushes the object out of the conveyor belt to its side.
  Everything returns to the initial state once the object is removed until the next object.

## Slide 12
SUBMITTABLES:
Media files:
https://drive.google.com/drive/folders/1bgYFixWVUVUYeKh3d1oyoI9kfAqogYM6?usp=sharing